## Slide 1: Power Turbine Systems: Tidal (Hydro / Under-sea) and Wind
        Linda Britt
        23 July 2015
        INCOSE Orlando Chapter October chapter meeting

## Slide 2: Power Sources
Making use of free 2/day tides
How much energy is in the tides vs in wind
How efficient is each type
% source 2003, 2006, 2009, 2012:
Scotland, 2015: 50% of electricity from Renewables

## Slide 3: Tidal, Hydro, Under-sea Turbines
Making use of free 2/day tides
How much energy is in the tides vs in wind
How efficient is each type

## Slide 4
What Causes the Tides?
The gravitational pull of the Moon and Tidal Inertia
The Sun’s gravitational pull also influences tides

## Slide 5
Changes in the angle of the Moon result in changes in the heights of tides (both high and low tides)

## Slide 6
LUNAR DAY
24 Hrs + 50 min
2 high tides
every 12 hrs + 25 min
2 low tides
every 12 hrs + 25 min
MOON

## Slide 7
TIDAL VARIATION Lunar Tides +/- Solar Tides
Spring Tides = Alignment of Moon & Sun
Neap Tides = Mis-alignment of Moon & Sun

## Slide 8
Low Tide 0.5m. below MLW
High Tide 2.5m above MLW
For every meter of rise and fall of tide over every square kilometer of the sea one million ton of water will flow every six hours (24/(in,out,in,out)=6). This water has kinetic energy that can be harnessed to generate electricity
This estuary is 5km long and 1 km wide.
Average Tides are 3m rise and fall
Volume: EVERY TIDE ...... 5 x 1 x 3 million ton of water go in (or out) this small estuary

## Slide 9: Tidal (vs Wind) decision: Sea water is ~ 825 times more dense than air. In order to achieve equivalent power: lesser blade-swept area required lesser velocity of blades required lesser number of turbines (in an array) required However Which is better where?: Example U.S.A.: large single mass land area=> 1 large perimeter (flow route)=>much energy, but large monitoring and collection range (, reef issues, cost to replace systems already in place,...) - consider difficulty and cost. Example UK: ~80 islands=> multiple and diverse paths = large cumulative perimeter => much energy in small-area accessible collection range(s).
Turbine power
P = ½ p AV3 x an efficiency factor
P=Power p=density of medium
V=velocity in metres/sec A=swept area
Air density ~1.2473 kg/m3 Seawater density ~1030 kg/m3

## Slide 10
TIMES OF HIGH WATER
(relative to Dover)
PLYMOUTH -5:40
SOUTHAMPTON 0;+2:00
DOVER 0
LONDON +2:45
HULL -5:10
NEWCASTLE +4:30
EDINBURGH +3:50
ORKNEY -0:45
BELFAST -0:10
LIVERPOOL 0
BRISTOL -4:15
At any hour of within any 24 hour period around the UK there would be several locations capable of generating (useful) electricity .

## Slide 11
USING THE TIDAL RESOURCE TO GENERATE BASELOAD ELECTRICITY
HW
HW
LW
RANGE
INTERVAL
Rule of 12ths
1 1/12th of tidal rise or fall
2 2/12th of tidal rise or fall
3 3/12th of tidal rise or fall
4 3/12th of tidal rise or fall
5 2/12th of tidal rise or fall
6 1/12th of tidal rise or fall
HW
A
LW
B
C
A
A
C
B
A
TIDAL POWER GENERATION
During the tidal cycles at locations A,B and C each generates maximum power during a two hour period on the respective flood tides; because high water is at different times there is continuous electricity outputs.

## Slide 12
Velocity m/s | Velocity knots | Marine kW/m2 | Wind kW/m2
1 | 2 1.96 | 0.52 | 
2 | 4 3.92 | 4.12 | 0.00499
3 | 6 5.88 | 13.91 | 0.01684
15 | 30 29.41 | 1738 | 2.1
20 | 40 39.22 | 4120 | 4.99
The kinetic energy of water is a function of velocity (speed) and mass.
ENERGY DENSITY
Sea water is ~ 825 times more dense than air; thus a current of only 2 m/s would correspond to the energy density at a wind speed of 18 m/s... given same scale turbines and ideal, 100% availability conditions.
ISLAND DENSITY Example
Pictured is only 1/4 of the west coast showing 43 islands!
Compare Power density (w/m2) for wind and water at same/similar velocities: (consider Area=1)
(1 knot = 1 nautical mile per hour = 1.15 statute mile per hour = .51m/s below (thus 1:2 column ratio))
Dr. Bahaj (Sustainable Energy Research Group, University of Southampton),
“a tidal current turbine rated to work in a flow between 2 to 3 metres/per second in seawater can typically access four times as much energy per rotor swept area as a similarly rated power wind turbine.”

## Slide 14
In 2004 the Marine Energy Group
confirmed 7.5 GW of tidal stream
potential (cost: ~10 cents per kWh)
This potential would generate 33.5 TWh
(or 98% of shown area’s annual
electricity consumption)
(20.9 TWh using the 6hr/day rule of thumb; 60%)
Verification report:
The Carbon Trust concluded that the total extractable UK resource is ~18 TWh per annum. (Thus 50% of consumption)

## Slide 15
Dark (red) shows highest velocity (and therefore energy); thus optimal turbine locations.
These are coastal locations having logistic and safety advantages. (Turbines are well below ship and sea-life activity. Slow moving (due to increased power/velocity) pose no harm to deep sea-life.
Hydro Turbine power
P = ½ p AV3 L
P=Power p=density of water
V=velocity in metres/sec A=swept area L = Load factor
Air density 1.2473 kg/m3 Seawater density 1030 kg/m3

## Slide 17
VENTURI
Types of turbines
Re: how the turbine is aligned to the medium: Horizontal Axis (HAWT) Vertical Axis (VAWT)
dual HAWT
OSCILLATING mechanical maintenance risks
VAWT

## Slide 18
Types of Anchoring
Seabed Mounted/Gravity Base
Pile Mounted
Floating
Flexible mooring
Rigid mooring
Floating structure
Hydrofoil Inducing Downforce

## Slide 19
FUNDAMENTAL RESEARCH
DEMONSTRATION PROJECT
APPLIED RESEARCH & DEVELOPMENT
PROTOTYPE
COMMERCIAL DEVELOPMENT
< STAGES IN TECHNOLOGICAL DEVELOPMENT
v Cost comparative over time

## Slide 20
Project example: 2011 initiated project by Scottish Power Renewables: ten 1MW tidal devices to be installed to generate ~ 30GWh per year.
This is equivalent to the annual electricity consumption of (a large island) or the electricity used by 5000 average UK houses.
For larger future projects the need will be large investments in grid connections. (Cost risk: Known durability issue for sub-marine cabling: abrasion by tidal currents.)

## Slide 21
Base of the assembly: 22 meter high to the hub.
Blades: ~ 11.5 meter long.
= Total height: 33.5 meter.
Design advantage: Tidal turbines do not turn to face into the tidal flow; rather individual blades turn around to face the flow.
During peak flow (3m/sec +) at Spring tides, the blades will rotate at ~ 10 times per minute; the tip of the blade would move at ~ 10 m/sec.
One of the main cost areas of marine renewables is in building custom installation platforms or barges.
Installation site example: Re-installing 300kW prototype Kvalsund, Norway 2009.

## Slide 22
The MeyGen project will consist of up to qty 400 1MW turbines.
They will be located in roughly 3.5 sq. kms of the Inner Sound, which lies between the island of Stroma and the northern coast of mainland Scotland.
The potential for a significant commercial project of 200 MW or more installed capacity.
This scheme will roll a demonstration array project into full commercial development.
Example: INNER SOUND TIDAL SCHEME

## Slide 23
2011 proposal: The MeyGen project (qty 398 1MW turbines) uses the model AK-1000, which stands at 22.5m (73ft) tall, weighs 1,300 ton, the rotor diameter is 18m (59ft);
It has been designed as a dual bladed turbine;
Each turbine has a rating of 1MW;
The turbine turns at 6 to 8 rpm.
Turbine power P= ½ p AV3 L
P=Power p=density of sea water
V=velocity in m/s A=swept area L = Load factor
Seawater density 1030kg/m3

## Slide 24
24
2015 update:
By the early 2020s MeyGen Limited intends to deploy up to 398MW of offshore tidal turbines.
MeyGen will be the World’s largest commercial tidal array.
Atlantis, owner of the world’s largest planned tidal stream energy project, MeyGen Limited (“MeyGen”), announced that all conditions have been satisfied under the terms of the funding package announced on 21 August 2014. £51.3 million has been secured from syndicate members
Phase 1A of the project will comprise the installation of four (update to 6) 1.5 MW turbines offshore as well as the construction of the onshore infrastructure to support the project. Three of the turbines will be supplied by Andritz Hydro Hammerfest and one Lockheed Martin-designed turbine supplied by Atlantis*.
The total first phase (Phase 1) of the project (61 (update to 86 turbines, 86MW)) is expected to provide enough electricity for 42,000 houses with the first electricity anticipated to be delivered to the grid by 2016.
(*Andritz supplied first tide to grid turbines in 2004 of VHS300 2003 300kw 1.5GWh. HS1000 1MW in Emec Germany has generated 800MWh. Atlantis is using 1.5MW AR1500 (new take-off on the AR1000) turbine.)

## Slide 25
MeyGen 2015 update: The system of systems:
Steel tripod Ph I: gravity (vs or tubular (drilled) monopile)
200 ton moving equipment limit, so installation is in parts.
Ship haul of sea cable with floats; drop floats, cables repositioned to allow sea floor variances to protect cable from tides.
Tower connection via gravity stab connection alone.

## Slide 26
26
MeyGen 2015 update continued: The system of systems continued:
15km of 33kV underground cable to main distribution.
Nacelle transport: (note scale vs ship.) GPS used in siting drop.
Ready to use in 60minutes from leaving delivery ship’s deck.
2020 Phase 1 complete
Phase II 312MW
When completed, the project will include up to 269 turbines (update to ‘the remainder of 398’ for both phases) submerged on the seabed, generating enough energy for 175,000 houses.

## Slide 27: Power calculations
24
Tidal Turbine power
        P= ½ p A V3 L
        P=W
        p=density of sea water ~1030kg/m3
V=velocity in meters/sec A=swept area in m2 L = Load factor*
Wind Turbine Power
      P=1/2 ρ V3 π r2 in practice x Cp Betz constant .59
        P=Power
ρ = air density ~1.225kg / m3 at sea level π r2 = swept area in m2
V=velocity in meters/sec
        Notes:
        Power factor, efficiency factor, *loading factor in some example calcs simplified as 1. Capacity factor typically used as some lesser of Betz limit, example .4 wind, .24 farm wind, .35 sea.
German physicist Albert Betz concluded in 1919 that no wind turbine can convert more than 16/27 (59.3%) of the kinetic energy of the wind into mechanical energy turning a rotor. To this day, this is known as the Betz Limit or Betz' Law.
Any moving mass carries Kinetic Energy in Joules = 0.5 x Mass x Velocity2 where mass = VpA x time, and 1 W = 1 Joulesec
Sea water/air ratio: 1030kg/m3 / 1.2473 kg/m3 roughly 825

## Slide 28: Early Water and Wind Power
25
Remember the Watermill / Grainmill
  flowing stream or river water turned cupped-blades, whose rotating vortex rod turned mill-building-interior turning grain mashers
Remember the Windmill
  Large area blades; local use of wind-to-power conversion
Risk points for both: gear assemblies.
  Today’s modern turbine-risks still include the gear assembles.
25

## Slide 29: Wind Turbines
26
On-land
Offshore
Blades are airborne; anchoring and half-turbine can be above ground or underwater (off-shore)
In 2011, Wind Power provided % electricity: Denmark 26%, Spain & Portugal 16%, Ireland 12%, Germany 11%
26

## Slide 30: Wind Turbines
27
Wind Turbine Types:
re: how the turbine is aligned to the wind:
  Horizontal Axis Wind Turbines (HAWT)
  Vertical Axis Wind Turbines (VAWT)
    Darrieus uses lift forces generated by aerofoils
      The Giromill is a variant of the Darrieus type
    Savonius uses drag forces (pushing)
      Operate in the same way as a cup anemometer.
      Typically only have an efficiency of ~15-20%
      Applications such as pumping water and grinding grain for which slow rotation and high torque (turning force) are essential.
    HAWT: suitable for large scale electricity generation fed into the grid. HAWTs have higher efficiency ratings in use and are best suited to operate in clear air. They need towers to position the turbine blades above turbulent air flow nearer the ground. They are not as efficient in turbulent air.
    VAWT: useful for lower output building fixed locations. Savonius turbines ( a type of VAWT) have the benefit that they continue to generate electricity in the strongest winds without being damaged
27

## Slide 31: Wind Turbines
27
Vertical Axis Wind Turbines (VAWT)
27

## Slide 32: Wind Turbines
27
Horizontal Axis Wind Turbines (HAWT)
  Tower
  Nacelle
  Blades assembly
  Rotor Assy
27

## Slide 33: Wind Turbines
27
27

## Slide 34: Wind Turbine Assembly
28
Sustainment:
  Blade
  Gearbox
  Generator
  A-D-A converters
  Circuit breaker
  Step-up transformer
28

## Slide 35: Wind Turbine Assembly
29
Sustainment:
  Blade
  Gearbox none required for direct drive models!
  Generator
  A-D-A converters
  Circuit breaker
  Step-up transformer
Type IV variable speed
Permanent magnet design
conversion to electricity efficiencies approach 40%
29
--------------------------------

## Slide 36: Wind Power - locations
30
Wind turbine best locations For U.S.A.
  wind performance - see area, blue
  power capacity in MW - see state, green dark =1GW to 10.2GW
    Source: NREL Wind Energy Resource Atlas of the U.S.

## Slide 37: Wind Power - summary
30
Advantages
  For U.S.A.: field area versus perimeter
  More mature technology
  Installation (vs Tidal)
Limitations
  For U.S.A.: High ground mid-west is best suited
Disadvantages
  Less Power to the grid (than Tidal); low wind carry-thru power may be required (V, velocity of equation, varies)
  Disruptive to scenery
Neutral comparative points
  Maintenance at heights
  Both wind and tidal provide no risk to air/sea-life
30

## Slide 38: Tidal Power - summary
31
Advantages
  Capable of more Power provided to the grid than wind
  For island nations: perimeter versus field area
  Non-disruptive to scenery
Limitations
  For U.S.A.: cannot be used in reef perimeter areas
Disadvantages
  For U.S.A.: (large) perimeter versus (accessible) field area
  Installation
  Maintenance
Neutral comparative points
  Maintenance under water
  Both wind and tidal provide no risk to air/sea-life
31

## Slide 39: Power Variance
31
Methodology
There are three methods for establishing the UK tidal stream resource:
Kinetic Energy Flux Black and Veatch for Carbon Trust
Bottom Friction Prof Stephen Salter
Shallow Wave Model Prof David JC Mackay
(Marine Energy Group)
(Offshore Evaluation Group)
31

## Slide 40: Power Variance continued
31
Terms: estimates of capacity in MW and provisions for a year in MWh
Nominal calculations often simplify Power factor, efficiency factor, loading factor as 1.
Betz limit: (wind) obtainable is only x .59 ideal. Tidal use Betz and/or a Load factor. A ‘Capacity factor’ is typically used as some lesser of Betz limit, example .4 wind, .24 farm wind, .35 to .5 marine. The capacity factor is typically shown as the final efficiency factor.
Wind velocity may be somewhat predicted daily, but cannot be committed within P = ....V3... equation.
Density of air varies with temperature, pressure, altitude (dry air at sea level, 20°C ~1.2 kg/m3. varying with pressure and temperature. (nom 1.225 kg/m3)
Density of water varies with temperature (seawater is more dense nom. 1030 kg/m3):
  example: Temp (°C) Density (kg/m3)
    +100 958.4 +80 971.8 +60 983.2 +40 992.2 +30 995.6502 +25 997.0479 +22 997.7735 +20 998.2071 +15 999.1026 +10 999.7026 +4 999.9720 0 999.8395 −10 998.117 −20 993.547 −30 983.854
31

## Slide 41: References
32
‘Hydro Power, Tidal Power’ (Under sea turbines) - T. Philpin, L. Britt 15 Sept 2011
Current Practices in Wind Power (Wind turbines) - R. Nelson 19 April 2012
Alienergy
International Energy Agency
Renewable Energy Systems
Scottish Renewables
usa.siemens.com
NREL Wind Energy Resource Atlas of the U.S.
Marine Current Turbines Limited, Atlas company
Dr. Bahaj, Sustainable Energy Research Group, University of Southampton
European Wind Energy Association
Linda Britt is an Electrical and Systems Engineer, serving on the Board of Directors for INCOSE Orlando Chapter since 2010; graduate of Drexel University, design engineer and manager for RCA, GE, NGC, among other companies. GGLINC11@gmail.com
32